## Slide 1: CSCI-351 Data communication and Networks
Lecture 11: Middleboxes and NAT
(Duct tape for IPv4)
The slide is built with the help of Prof. Alan Mislove, Christo Wilson, and David Choffnes's class

## Slide 2: Middleboxes
Devices in the network that interact with network traffic from the IP layer and up
Common functions
  NAT
  Firewall and other security
  Proxy
  Filtering
  Caching
  …
Internet
Notes: Doesn’t have to be a physical thing

## Slide 3: Outline
NAT
Other middleboxes

## Slide 4: The IPv4 Shortage
Problem: consumer ISPs typically only give one IP address per-household
  Additional IPs cost extra
  More IPs may not be available
Today’s households have more networked devices than ever
  Laptops and desktops
  TV, bluray players, game consoles
  Tablets, smartphones, eReaders
How to get all these devices online?

## Slide 5: Private IP Networks
Idea: create a range of private IPs that are separate from the rest of the network
  Use the private IPs for internal routing
  Use a special router to bridge the LAN and the WAN
Properties of private IPs
  Not globally unique
  Usually taken from non-routable IP ranges (why?)
Typical private IP ranges
  10.0.0.0 – 10.255.255.255
  172.16.0.0 – 172.31.255.255
  192.168.0.0 – 192.168.255.255

## Slide 6: Private Networks
Private
Network
192.168.0.1
192.168.0.0
66.31.210.69
NAT
192.168.0.2
Private
Network
192.168.0.2
192.168.0.1
Internet
192.168.0.0

## Slide 7: Network Address Translation (NAT)
NAT allows hosts on a private network to communicate with the Internet
  Warning: connectivity is not seamless
Special router at the boundary of a private network
  Replaces internal IPs with external IP
    This is “Network Address Translation”
  May also replace TCP/UDP port numbers
Maintains a table of active flows
  Outgoing packets initialize a table entry
  Incoming packets are rewritten based on the table

## Slide 8: Basic NAT Operation
Private Network
Internet
Source: 192.168.0.1
Dest: 74.125.228.67
Source: 66.31.210.69
Dest: 74.125.228.67
66.31.210.69
Source: 74.125.228.67
Dest: 66.31.210.69
74.125.228.67
192.168.0.1
Source: 74.125.228.67
Dest: 192.168.0.1
Private Address | Public Address
192.168.0.1:2345 | 74.125.228.67:80

## Slide 9: Advantages of NATs
Allow multiple hosts to share a single public IP
Allow migration between ISPs
  Even if the public IP address changes, you don’t need to reconfigure the machines on the LAN
Load balancing
  Forward traffic from a single public IP to multiple private hosts

## Slide 10: Natural Firewall
Private Network
Internet
66.31.210.69
Source: 74.125.228.67
Dest: 192.168.0.1
74.125.228.67
192.168.0.1
Private Address | Public Address
Source: 74.125.228.67
Dest: 66.31.210.69

## Slide 11: Concerns About NAT
Performance/scalability issues
  Per flow state!
  Modifying IP and Port numbers means NAT must recompute IP and TCP checksums
Breaks the layered network abstraction
Breaks end-to-end Internet connectivity
  192.168.*.* addresses are private
  Cannot be routed to on the Internet
  Problem is worse when both hosts are behind NATs

## Slide 12: Port Forwarding
Private Network
Internet
66.31.210.69
Source: 74.125.228.67:8679
Dest: 66.31.210.69:7000
74.125.228.67
192.168.0.1
Source: 74.125.228.67:8679
Dest: 192.168.0.1:7000
Private Address | Public Address
192.168.0.1:7000 | *.*.*.*:*
Notes: 66.31.210.69:3389

## Slide 13: Outline
NAT
Other middleboxes

## Slide 14: Firewall
A device that blocks traffic according to a set of rules
  Why?
  Services with vulnerabilities turned on by default
  ISP policy forbidding certain traffic due to ToS
Typically specified using a 5-tuple
  E.g., block outbound SMTP; block inbound SQL server reqs
GFC (Great Firewall of China)
  Known to block based on IP, filter DNS requests, etc
Notes: Protocol number

## Slide 15: Web caching
ISP installs cache near network edge that caches copies of Web pages
  Why?
  Performance: Content is closer to clients, TCP will perform better with lower RTTs
  Cost: “free” for the ISP to serve from inside the network
Limitations
  Much of today’s content is not static (why does this matter?)
  Content ownership
  Potential privacy issues
  Long tail of content popularity

## Slide 16: Web caching
ISP installs cache near network edge that caches copies of Web pages
  Why?
  Performance: Content is closer to clients, TCP will perform better with lower RTTs
  Cost: “free” for the ISP to serve from inside the network
Internet
foo.htm
Not cached
foo.htm

## Slide 17: Proxying
Non-split connections
  Like NAT, but IP address is no longer the one assigned to you
Split connections
  Middlebox maintains two flows: C-M and M-S
  Can be done transparently
    How?
C
S
M
Syn
Syn
Ack
Ack
SynAck
SynAck

## Slide 18: Proxying
Advantages
  RTT is lower on each end
  Can use different MTUs
  Particularly useful in cell ntwks
Disadvantages
  Extra delay can be bad for small flows
  Buffering/state makes it potentially costly
C
S
M
Syn
Syn
Ack
Ack
SynAck
SynAck

## Slide 19: Questions
Middleboxes that breaks end-to-end integrity
How can we tell if middle boxes do that?
  ISP? Software on your computer? How can we tell that?

## Slide 20: CSCI-351 Data communication and Networks
Lecture 11 ext: DHCP
The slide is built with the Prof. Kurose’s materials

## Slide 21: DHCP: Dynamic Host Configuration Protocol
Let’s say that a ISP has X customers, How many IPs does it need to have?
  X?
Goal: allow host to dynamically obtain its IP address from network server when it joins network
  can renew its lease on address in use
  allows reuse of addresses (only hold address while connected/“on”)
  support for mobile users who want to join network (more shortly)

## Slide 22: DHCP Client-Server

## Slide 23: DHCP Client-Server
DHCP server: 223.1.2.5
arriving
client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I’ll take that IP address!
Broadcast: OK. You’ve got that IP address!
Notes: Your IP address

## Slide 24: DHCP: More than IP address
DHCP can return more than just allocated IP address on subnet
  address of first-hop router for client
  name and IP address of DNS sever
  network mask (indicating network versus host portion of address)

## Slide 25: DHCP Header (Do not memorize)

## Slide 26: DHCP: example
router with DHCP
server built into
router
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.1 Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demuxed to IP demuxed, UDP demuxed to DHCP
168.1.1.1
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
connecting laptop needs its IP address, addr of first-hop router, addr of DNS server: use DHCP

## Slide 27: DHCP: example
encapsulation of DHCP server, frame forwarded to client, demuxing up to DHCP at client
router with DHCP
server built into
router
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
client now knows its IP address, name and IP address of DSN server, IP address of its first-hop router
DCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server