## Slide 1: CSCI-351 Data communication and Networks
Lecture 3: Internet Architecture
(Big picture of how Internet works)
The slide is built with the help of Prof. Alan Mislove, Christo Wilson, and David Choffnes's class

## Slide 2: Recap

## Slide 3: Okay, what are we going to study?
Application
Transport
Network
Data Link
Physical

## Slide 4: Okay, what are we going to study?
Application
Transport
Network
Data Link
Physical
Packet
John: Hi there
?
Datagram
Packet

## Slide 5: CSCI-351 Data communication and Networks
Lecture 3: Internet Architecture
(Big picture of how Internet works)
The slide is built with the help of Prof. Alan Mislove, Christo Wilson, and David Choffnes's class

## Slide 6: Organizing Network Functionality
Networks are built from many components
  Networking technologies
  Network styles
  Applications
How do we make all this stuff work together?!
Ethernet, Wifi, Bluetooth, Fiber Optic, Cable Modem, DSL
Circuit switch, packet switch
Wired, Wireless, Optical, Satellite
Email, Web (HTTP), FTP, BitTorrent, VoIP
Notes: - Network technologies: desktop? laptop? Credit card, NFC? (Near Field Communication)
- switch?

## Slide 7: Problem Scenario
Web
Email
Bittorrent
Ethernet
802.11
Bluetooth
VoIP
Cellular
This is a nightmare scenario
Huge amounts of work to add new apps or media
Limits growth and adoption
Notes: Let’s say you build an web application, then what do you need to do?
Layout, human interfaces,

## Slide 8: More Problems
Bittorrent
Ethernet
802.11
Bittorrent
Application endpoints may not be on the same media
Notes: Then what’s the solution?

## Slide 9: Solution:
Web
Email
Bittorrent
Ethernet
802.11
Bluetooth
Magical Network Abstraction Layer
Notes: What’s the complexity to add new application or new medium?
Order of N, N^2

## Slide 10: Solution: Use Indirection
Web
Email
Bittorrent
Ethernet
802.11
Bluetooth
VoIP
Cellular
Magical Network Abstraction Layer
O(1) work to add new apps, media
Few limits on new technology
API
API
API
API
Notes: What’s the complexity to add new application or new medium?
Order of N, N^2

## Slide 11: Layered Network Stack
  Does not specify an implementation
  Instead, tells us how to organize functionality
Applications
Physical
Media
Layer N
Layer 1
Layer 2
…
  Interfaces define cross-layer interaction
  Layers only rely on those below them
Encapsulation
Modularity
Flexibility
  Reuse of code across the network
  Module implementations may change
Unfortunately, there are tradeoffs
  Interfaces hide information
  As we will see, may hurt performance…
Notes: That’s why we need layering.
So each layer does not specify an implementation; instead it just want you to pass “this this this” information.
Do you know how to call it?
Second, interfaces define cross-layer interaction.
Also, one layer doest not care about other layers but neighbor layers.
Abstraction. Does it remind you something in programming language? Java? C++? Abstract class,

## Slide 12: Key Questions
How do we divide functionality into layers?
  Routing
  Congestion control
  Error checking
How do we distribute functionality across devices?
  Example: who is responsible for sanity check?
Switch
Switch
Router
  Security
  Fairness
  And many more…
Notes: Every networking devices does not need to implement all of these functionalities.
Your machine does not need to have a routing of course.
Congestion control - interfere

## Slide 13: Outline
Layering
  The OSI Model
Communicating
  The End-to-End Argument
Notes: International Organization for Standardization (ISO)
Standardization organization

## Slide 14: The ISO OSI Model
OSI: Open Systems Interconnect Model
Application
Presentation
Session
Transport
Network
Data Link
Physical
Network
Data Link
Application
Presentation
Session
Transport
Network
Data Link
Physical
Host 1
Router
Host 2
Physical
Application
Presentation
Session
Transport
Notes: Host1 and host2 communicates
Of course, we need a router to pass the packets
3. Then, Do routers also need to implement all the layer’s functionality?
What is the core example of the network layer?

## Slide 15: The ISO OSI Model
OSI: Open Systems Interconnect Model
Application
Presentation
Session
Transport
Network
Data Link
Physical
Network
Data Link
Application
Presentation
Session
Transport
Network
Data Link
Physical
Host 1
Router
Host 2
Physical
All devices implement the first three layers
Layers communicate peer-to-peer
Layers communicate peer-to-peer

## Slide 16: Layer Features
Service
  What does this layer do?
Interface
  How do you access this layer?
Protocol
  How is this layer implemented?
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 17: Physical Layer
Service
  Move information between two systems connected by a physical link
Interface
  Specifies how to send one bit
Protocol
  Encoding scheme for one bit
  Voltage levels
  Timing of signals
Examples: coaxial cable, fiber optics, radio frequency transmitters
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 18: Data Link Layer
Service
  Data framing: boundaries between packets
  Media access control (MAC)
  Per-hop reliability and flow-control
Interface
  Send one packet between two hosts connected to the same media
Protocol
  Physical addressing (e.g. MAC address)
Examples: Ethernet, Wifi
Application
Presentation
Session
Transport
Network
Data Link
Physical
Notes: Each device has an unique ID of Mac address, and this ID must be unique in the local network.
So if you’re connected same RIT wifi network, and some of you happen to have the same Mac address? Then you will not be able to use the Internet, because the data supposed to be sent to you, may be sent to someone else.
Does anyone know good example of how this Mac address is used in practice?
If you goto the airport, some airport give you an free internet access just for an hour, after that
Open WIFI? TERMS OF SERVICES?

## Slide 19: Network Layer
Service
  Deliver packets across the network
  Handle fragmentation/reassembly
  Packet scheduling
  Buffer management
Interface
  Send one packet to a specific destination
Protocol
  Define globally unique addresses
  Maintain routing tables
Example: Internet Protocol (IP), IPv6
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 20: Transport Layer
Service
  Multiplexing/demultiplexing
  Congestion control
  Reliable, in-order delivery
Interface
  Send message to a destination
Protocol
  Port numbers
  Reliability/error correction
  Flow-control information
Examples: UDP, TCP
Application
Presentation
Session
Transport
Network
Data Link
Physical
Notes: Mux and Demux
“Digital Circuit” or “Microprocessor” class

## Slide 21: Session Layer
Service
  Access management
  Synchronization
Interface
  It depends…
Protocol
  Token management
  Insert checkpoints
Examples: none
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 22: Presentation Layer
Service
  Convert data between different representations
  E.g. big endian to little endian
  E.g. Ascii to Unicode
Interface
  It depends…
Protocol
  Define data formats
  Apply transformation rules
Examples: none
Application
Presentation
Session
Transport
Network
Data Link
Physical
Notes: Digital circuit/ digital electronics?
Little endian = intel
0x12345678: 4 byte integer
bigEndian: 12/34/56/78
Little:
Memory address unit (A word)
ASCII: 128, Unicode: 2^21 two to the twenty one

## Slide 23: Application Layer
Service
Interface
Protocol
Examples:
Application
Presentation
Session
Transport
Network
Data Link
Physical
  Whatever you want :)
  Whatever you want :D
  Whatever you want ;)
turn on your smartphone and look at the list of apps

## Slide 24: Encapsulation
How does data move through the layers?
Application
Presentation
Session
Transport
Network
Data Link
Physical
Data
Data
Notes: WHY????

## Slide 25: Real Life Analogy
Notes: Do you have any idea of real life analogy?
What is the similar concept of this one in real life?
Layering, encapsulation

## Slide 26: Real Life Analogy
Postal Service
Label contains routing info
Un-packing
Doesn’t know contents of letter
Doesn’t know how the Postal network works

## Slide 27: Network Stack in Practice
Application
Presentation
Session
Transport
Network
Data Link
Physical
Network
Data Link
Application
Presentation
Session
Transport
Network
Data Link
Physical
Host 1
Router
Host 2
Physical
Video Client
UDP
Video Server
UDP
FTP Client
TCP
IP
Ethernet
IP
Ethernet
FTP Server
TCP
IP
Ethernet
802.11n
802.11n
802.11n

## Slide 28: Encapsulation, Revisited
Web Server
TCP
IP
Ethernet
HTTP Header
TCP Header
IP Header
Ethernet Header
Ethernet Trailer
Web Page
HTTP Header
Web Page
TCP Header
HTTP Header
Web Page
IP Header
TCP Header
HTTP Header
Web Page
TCP Segment
IP Datagram
Ethernet Frame
Notes: WHY???

## Slide 29: The Hourglass
IPv4
TCP, UDP, ICMP
HTTP, FTP, RTP, IMAP, Jabber, …
Ethernet, 802.11x, DOCSIS, …
Fiber, Coax, Twisted Pair, Radio, …
One Internet layer means all networks interoperate
All applications function on all networks
Room for development above and below IP
But, changing IP is insanely hard
Think about the difficulty of deploying IPv6…

## Slide 30: An Example of the New Architectures Named Data Networking (NDN)
Notes: Let me ask you something,
What do you usually do on the Internet? Content
When do you watch a video on Netflix, the server must have the IP address, and your phone and machine must have the IP address, right?
When you watch the video, do you care about the IP? Do you know where it comes from? Most importantly do you care?
2006 named data networking
the idea was very simple; hey you know what; I’ve just learned that we actually do not care about the IP; but we only care about the content!

## Slide 31: Orthogonal Planes
Application
Presentation
Session
Transport
IP
Data Link
Physical
BGP
RIP
OSPF
Control Plane
Well cover this later…
Control plane: How Internet paths are established

## Slide 32: Orthogonal Planes
Application
Transport
Network
Data Link
Network
Data Link
Host 1
Switch(es)
Host 2
Application
Transport
Network
Data Link
Data plane: How data is forwarded over Internet paths

## Slide 33: Reality Check
The layered abstraction is very nice
Does it hold in reality?
No. (Any examples?)
Firewalls
Analyze application layer headers
Transparent Proxies
Simulate application endpoints within the network
NATs
Break end-to-end network reachability
Notes: Sometimes you input the wrong domain name on your browser, and the content is like “hey this is the result of your domain searching”

## Slide 34: Outline
Layering
  The OSI Model
Communicating
  The End-to-End Argument

## Slide 35: From Layers to Eating Cake
IP gives us best-effort datagram forwarding
  So simple anyone can do it
  Large part of why the Internet has succeeded
  …but it sure isn’t giving us much
Layers give us a way to compose functionality
  Example: HTTP over TCP for Web browsers with reliable connections
…but they do not tell us where (in the network) to implement the functionality

## Slide 36: Where to Place Functionality
How do we distribute functionality across devices?
  Example: who is responsible for security?
Switch
Switch
Router
?
?
?
?
?
“The End-to-End Arguments in System Design”
  Saltzer, Reed, and Clark
  The Sacred Text of the Internet
  Endlessly debated by researchers and engineers

## Slide 37: Basic Observation
Some applications have end-to-end requirements
  Security, reliability, etc.
Implementing this stuff inside the network is hard
  Every step along the way must be fail-proof
  Different applications have different needs
End hosts…
  Can’t depend on the network
  Can satisfy these requirements without network level support

## Slide 38: Example: Reliable File Transfer
Solution 1: Make the network reliable
Solution 2: App level, end-to-end check, retry on failure
Integrity Check
Integrity Check
Integrity Check
App has to do a check anyway!

## Slide 39: Example: Reliable File Transfer
Solution 1: Make the network reliable
Solution 2: App level, end-to-end check, retry on failure
Please Retry
Full functionality can be built at App level
In-network implementation…
  Doesn’t reduce host complexity
  Does increase network complexity
  Increased overhead for apps that don’t need functionality
But, in-network performance may be better

## Slide 40: Conservative Interpretation
“Don’t implement a function at the lower levels of the system unless it can be completely implemented at this level” (Peterson and Davie)
Basically, unless you can completely remove the burden from end hosts, don’t bother

## Slide 41: Radical Interpretation
Don’t implement anything in the network that can be implemented correctly by the hosts
Make network layer absolutely minimal
Ignore performance issues

## Slide 42: Moderate Interpretation
Think twice before implementing functionality in the network
If hosts can implement functionality correctly, implement it a lower layer only as a performance enhancement
But do so only if it does not impose burden on applications that do not require that functionality…
…and if it doesn’t cost too much $ to implement

## Slide 43: Reality Check, Again
Layering and E2E principals regularly violated
Firewalls
Transparent Proxies
NATs
Conflicting interests
  Architectural purity
  Commercial necessity

## Slide 44: Real world example (DNS Hijacking)
Browser
DNS Server
NXDOMAIN
non-exist-url.com
404 Not Found!
Advertisement or
other contents

## Slide 45
Country | ISP | DNS Servers | Exit Nodes
Argentina | Telefonica de Argentina | 14 | 276
Australia | Dodo Australia | 21 | 1,404
Brazil | Oi Fixo | 21 | 2,558
 | CTBC | 4 | 290
Germany | Deutsche Telekom | 8 | 1,385
India | Airtel Broadband | 9 | 735
 | BSNL | 2 | 71
 | Ntl. Int. Backbone | 8 | 245
Malyasia | TMNet | 8 | 1,676
Spain | Ono | 2 | 71
U.K. | BT Internet | 6 | 479
 | Talk Talk | 46 | 3,738
U.S. | AT&T | 37 | 561
 | Cable One | 4 | 108
 | Cox Communications | 63 | 1,789
 | Mediacom Cable | 6 | 219
 | Suddenlink | 9 | 98
 | Verizon | 98 | 2,102
 | WideOpen West | 1 | 39
Real world example (DNS Hijacking)
Tunneling for Transparency: A Large-Scale Analysis of End-to-End Violations in the Internet
Taejoong Chung, David Choffnes, and Alan Mislove
In Proceedings of ACM Internet Measurement Conference (IMC`16), Santa Monica, California, USA, November 2016

## Slide 47: Takeaways
Layering for network functions
  Helps manage diversity in computer networks
  Not optimal for everything, but simple and flexible
Narrow waist ensures interoperability, enables innovation
E2E argument (attempts) to keep IP layer simple
Think carefully when adding functionality into the network

## Slide 48: Questions?

## Slide 49: Next Class..
C-Socket Programming