## Slide 1: CSCI-351 Data communication and Networks
Lecture 9: Intra Domain Routing
The slide is built with the help of Prof. Alan Mislove, Christo Wilson, and David Choffnes's class

## Slide 2: Network Layer, Control Plane
Function:
  Set up routes within a single network
Key challenges:
  Distributing and updating routes
  Convergence time
  Avoiding loops
Application
Presentation
Session
Transport
Network
Data Link
Physical
BGP
RIP
OSPF
Control Plane
Data Plane

## Slide 3: Internet Routing
Internet organized as a two level hierarchy
First level – autonomous systems (AS’s)
  AS – region of network under a single administrative domain
  Examples: Comcast, AT&T, Verizon, Sprint, etc.
AS’s use intra-domain routing protocols internally
  Distance Vector, e.g., Routing Information Protocol (RIP)
  Link State, e.g., Open Shortest Path First (OSPF)
Connections between AS’s use inter-domain routing protocols
  Border Gateway Routing (BGP)
  De facto standard today, BGP-4
Notes: Different MTU for each network.

## Slide 4: AS Example
AS-1
AS-2
AS-3
Interior Routers
BGP Routers

## Slide 5: Why Do We Need ASs?
Routing algorithms are not efficient enough to execute on the entire Internet topology
Different organizations may use different routing policies
Allows organizations to hide their internal network structure
Allows organizations to choose how to route across each other (BGP)
Notes: Directly related to their business model and security (Structure)

## Slide 6: Routing on a Graph (Intra –)
Goal: determine a “good” path through the network from source to destination
What is a good path?
  Usually means the shortest path
  Load balanced
  Lowest $$$ cost
Network modeled as a graph
  Routers  nodes
  Link  edges
    Edge cost: delay, congestion level, etc.
A
B
C
D
E
F
5
2
3
5
2
1
1
2
3
1

## Slide 7: Routing Problems
Assume
  A network with N nodes
  Each node only knows
    Its immediate neighbors
    The cost to reach each neighbor
How does each node learn the shortest path to every other node?
A
B
C
D
E
F
5
2
3
5
2
1
1
2
3
1

## Slide 8: Intra-domain Routing Protocols
Distance vector
  Routing Information Protocol (RIP), based on Bellman-Ford
  Routers periodically exchange reachability information with neighbors
Link state
  Open Shortest Path First (OSPF), based on Dijkstra algorithm
  Each network periodically floods immediate reachability information to all other routers
  Per router local computation to determine full routes
8

## Slide 9: Outline
Distance Vector Routing
  RIP
Link State Routing
  OSPF
  IS-IS (Intermediate System to Intermediate System)
Notes: Intermediate System to Intermediate System

## Slide 10: Distance Vector Routing
What is a distance vector?
  Current best known cost to reach a destination
Idea: exchange vectors among neighbors to learn about lowest cost paths
Routing Information Protocol (RIP)
Destination | Cost
A | 7
B | 1
D | 2
E | 5
F | 1
DV Table
at Node C
No entry for C
Initially, it only has info for immediate neighbors
  Other destinations cost = ∞
Eventually, vector is filled

## Slide 11: Concept of Distance Vector Algorithm
Bellman-Ford equation (dynamic programming)
let
dx(y) := cost of least-cost path from x to y
then
dx(y) = min {c(x,v) + dv(y) }
cost to neighbor v
cost from neighbor v to destination y
min taken over all neighbors v of x

## Slide 12: Distance Vector Routing Algorithm
Wait for change in local link cost or message from neighbor
Recompute distance table
If least cost path to any destination has changed, notify neighbors

## Slide 13: Distance Vector Initialization
Dest. | Cost | Next
B | 2 | B
C | 7 | C
D | ∞ | 
2
3
1
A
B
C
D
1
7
Node A
Dest. | Cost | Next
A | 2 | A
C | 1 | C
D | 3 | D
Node B
Dest. | Cost | Next
A | 7 | A
B | 1 | B
D | 1 | D
Node C
Dest. | Cost | Next
A | ∞ | 
B | 3 | B
C | 1 | C
Node D
Initialization:
for all neighbors V do
if V adjacent to A
D(A, V) = c(A,V);
else
D(A, V) = ∞;
…

## Slide 14: Distance Vector: 1st Iteration
Dest. | Cost | Next
B | 2 | B
C | 7 | C
D | ∞ | 
2
3
1
A
B
C
D
1
7
Node A
Dest. | Cost | Next
A | 2 | A
C | 1 | C
D | 3 | D
Node B
Dest. | Cost | Next
A | 7 | A
B | 1 | B
D | 1 | D
Node C
Dest. | Cost | Next
A | ∞ | 
B | 3 | B
C | 1 | C
Node D
…
loop:
…
else if (update D(V, Y) received from V)
for all destinations Y do
D(A, Y) =
min(D(A, Y),
D(A, V) + D(V, Y));
if (there is a new min. for dest. Y)
send D(A, Y) to all neighbors
forever
8
C
D(A,D) = min(D(A,D), D(A,C)+D(C,D))
= min(∞, 7 + 1) = 8
3
B
5
B
D(A,C) = min(D(A,C), D(A,B)+D(B,C))
= min(7, 2 + 1) = 3
D(A,D) = min(D(A,D), D(A,B)+D(B,D))
= min(8, 2 + 3) = 5
2
C
4
B
3
B

## Slide 15: Distance Vector: End of 3rd Iteration
Dest. | Cost | Next
B | 2 | B
C | 3 | B
D | 4 | B
2
3
1
A
B
C
D
1
7
Node A
Dest. | Cost | Next
A | 2 | A
C | 1 | C
D | 2 | C
Node B
Dest. | Cost | Next
A | 3 | B
B | 1 | B
D | 1 | D
Node C
Dest. | Cost | Next
A | 4 | C
B | 2 | C
C | 1 | C
Node D
…
loop:
…
else if (update D(V, Y) received from V)
for all destinations Y do
D(A, Y) =
min(D(A, Y),
D(A, V) + D(V, Y));
if (there is a new min. for dest. Y)
send D(A, Y) to all neighbors
forever
Nothing changes, algorithm terminates
Until something changes…

## Slide 16
4
1
A
B
C
50
1
Node B
Node C
Time
D | C | N
A | 4 | A
C | 1 | B
D | C | N
A | 5 | B
B | 1 | B
D | C | N
A | 1 | A
C | 1 | B
D | C | N
A | 5 | B
B | 1 | B
D | C | N
A | 1 | A
C | 1 | B
D | C | N
A | 2 | B
B | 1 | B
D | C | N
A | 1 | A
C | 1 | B
D | C | N
A | 2 | B
B | 1 | B
Link Cost Changes,
Algorithm Starts
Algorithm Terminates
Good news travels fast
…
loop:
…
else if (update D(V, Y) received from V)
for all destinations Y do
D(A, Y) =
min(D(A, Y),
D(A, V) + D(V, Y));
if (there is a new min. for dest. Y)
send D(A, Y) to all neighbors
forever
Notes: Change circles to rectangles, don’t block the text

## Slide 17: Count to Infinity Problem
4
1
A
B
C
50
60
Node B
Node C
Time
D | C | N
A | 4 | A
C | 1 | B
D | C | N
A | 5 | B
B | 1 | B
D | C | N
A | 6 | C
C | 1 | B
D | C | N
A | 5 | B
B | 1 | B
D | C | N
A | 6 | C
C | 1 | B
D | C | N
A | 7 | B
B | 1 | B
D | C | N
A | 8 | C
C | 1 | B
D | C | N
A | 7 | B
B | 1 | B
Node B knows D(C, A) = 5
However, B does not know the path is C  B  A
Thus, D(B,A) = 6 !
Notes: Until
A 51 C
C 1 B
And
A 50 B
B 1 B
The problem of this algorithm is that, C tells B the cost to the path A even though they use a path C–B

## Slide 18: Count to Infinity Problem
4
1
A
B
C
50
60
Node B
Node C
Time
D | C | N
A | 51 | A
C | 1 | B
D | C | N
A | 50 | B
B | 1 | B
D | C | N
A | 50 | A
C | 1 | B
No Update and no advertisement.
Algorithm stops here.
Bad news travels slowly
Notes: Until
A 51 C
C 1 B
And
A 50 B
B 1 B
The problem of this algorithm is that, C tells B the cost to the path A even though they use a path C–B

## Slide 19: Why this is happening
Node B
Node C
D | C | N
A | 4 | A
C | 1 | B
D | C | N
A | 5 | B
B | 1 | B
D | C | N
A | 6 | C
C | 1 | B
D | C | N
A | 5 | B
B | 1 | B
4
1
A
B
C
50
60
Node B knows D(C, A) = 5
[Root Cause] B does not know the path is C  B  A
Thus, D(B,A) = 6 !
How can we prevent it?
=> C should let B know that C will forward the packet back to the B (which does not support in the DV protocol)
=> or C can just pretend that it does not have a path to the destination so that B will not forward the packet to C

## Slide 20: Poisoned Reverse
4
1
A
B
C
50
60
Node B
Node C
Time
D | C | N
A | 4 | A
C | 1 | B
D | C | N
A | 5 | B
B | 1 | B
D | C | N
A | 60 | A
C | 1 | B
D | C | N
A | 5 | B
B | 1 | B
D | C | N
A | 60 | A
C | 1 | B
D | C | N
A | 50 | A
B | 1 | B
D | C | N
A | 51 | C
C | 1 | B
D | C | N
A | 50 | A
B | 1 | B
If C routes through B to get to A
  C tells B that D(C, A) = ∞
    Pretending there is no direct route to A
  Thus, B won’t route to A via C
  D(C, A) = ∞
Notes: Even though C has this row; A – 5 – B; C tells that I do not have a path to A.

## Slide 21: Poison Reverse’s Limitation
A tells B & C that D is unreachable
B computes new route thorough C (B doesn’t know that A sent the same message to C)
  Tells C that D is reachable (poison reverse)
  Tells A it has a path of cost 3
A computes new route through B
  A tells C that D is now reachable
Loop..
1
1
1
A
B
C
D
1

## Slide 22: Outline
Distance Vector Routing
  RIP
Link State Routing
  OSPF
  IS-IS
Notes: What was the root cause of Distance Vector Routing? (They only know about the neighbor’s “cost” to another router)

## Slide 23: Link State Routing
Each node knows its connectivity and cost to direct neighbors
Each node tells every other node this information
Each node learns complete network topology
Use Dijkstra to compute shortest paths

## Slide 24: Flooding Details
Each node periodically generates Link State Packet
  ID of node generating the LSP
  List of direct neighbors and costs
  Sequence number (64-bit, assumed to never wrap)
  Time to live
Flood is reliable (ack + retransmission)
Sequence number “versions” each LSP
Receivers flood LSPs to their own neighbors
  Except whoever originated the LSP
LSPs also generated when link states change

## Slide 25: Dijkstra’s Algorithm
Step | Start S | B | C | D | E | F
0 | A | 2, A | 5, A | 1, A | ∞ | ∞
1 | AD |  | 4, D |  | 2, D | ∞
2 | ADE |  | 3, E |  |  | 4, E
3 | ADEB |  |  |  |  | 
4 | ADEBC |  |  |  |  | 
5 | ADEBCF |  |  |  |  | 
A
B
C
D
E
F
5
2
3
5
2
1
1
2
3
1
Initialization:
S = {A};
for all nodes v
if v adjacent to A
then D(v) = c(A,v);
else D(v) = ∞;
…
…
Loop
find w not in S s.t. D(w) is a minimum;
add w to S;
update D(v) for all v adjacent
  to w and not in S:
D(v) = min( D(v), D(w) + c(w,v) );
until all nodes in S;

## Slide 26: OSPF vs. IS-IS
Favored by companies, datacenters
More optional features
Built on top of IPv4
  LSAs are sent via IPv4
  OSPFv3 needed for IPv6
Favored by ISPs
Less “chatty”
  Less network overhead
  Supports more devices
Not tied to IP
  Works with IPv4 or IPv6
OSPF
IS-IS
Two different implementations of link-state routing
Notes: Authentication, address family,, and etc.

## Slide 27: Different Organizational Structure
OSPF
IS-IS
Area 0
Area 1
Area 2
Area 3
Area 4
Organized around overlapping areas
Area 0 is the core network
Organized as a 2-level hierarchy
Level 2 is the backbone
Level 2
Level 1
Level 1-2

## Slide 28: Link State vs. Distance Vector
 | Distance Vector | Link State
Message Complexity | O(d*n*k) | O(n2*e)
Time Complexity | O(n) | O(n*log n)
Convergence Time | O(k) | O(1)
Robustness | Nodes may advertise incorrect path cost Errors propagate due to sharing of DV tables | Nodes may advertise incorrect link costs Each node computes their own table
n = number of nodes in the graph
d = degree of a given node
k = number of rounds
Which is best?
In practice, it depends.
In general, link state is more popular.